## Slide 1: While you wait
Follow us on twitter - @pybamm_
Star us on GitHub - PyBaMM
Fill out the PyBaMM Survey - survey.pybamm.org
Try our online examples - colab.pybamm.org

## Slide 2: Python Battery Mathematical Modelling

## Slide 3: Why model batteries?
Not *that* much battery data (+ curse of dimensionality)
Electrochemical models can:
  Provide physical insight
  Be generalized
  Regularize data-driven methods
Need to be:
  Fast (enough)
  Easy to use, share, understand
  Reliable
Ultimately, will need hybrid approach
Batteries are complicated!
We have lots of data, why not just do machine learning?
Data-driven prediction of battery cycle life before capacity degradation. K.A. Severson et al., Nature Energy, 2019

## Slide 4: Why PyBaMM?
PyBaMM's mission is to accelerate battery modelling research
by providing an open-source framework for multi-institutional,
interdisciplinary collaboration.
Fostering a Sustainable Community in Batteries, J.A. Baker, M. Beuse, S.C. DeCaluwe, L.W. Jing, E. Khoo, S. Sripad, U. Ulissi, A. Verma, A.A. Wang, Y.T. Yeh, N. Yiu, D.A. Howey, and V. Viswanathan, ACS Energy Letters, 2020

## Slide 5: PyBaMM Goals
Provide fast, reliable battery simulations
Grow battery modelling user-base
Facilitate development of new battery models
Improve reproducibility of research

## Slide 6: Who is PyBaMM? Core Developers
Michigan
Mechanical Engineering
Warwick
Oxford
Maths
Computer science
UCL
Elec. Innovation Lab
WMG
PyBaMM
Faraday Institution
Imperial
Engineering

## Slide 7: Who is PyBaMM? Active and growing community
GitHub Interactions Data collected from publicly available location information github.com/pybamm-team/PyBaMM
Star
Fork

## Slide 8: Who is PyBaMM? Active and growing community
Number of website hits

## Slide 9: PYBAMM BASICS

## Slide 10: What is PyBaMM?
FAST
FLEXIBLE
RELIABLE
PyBaMM is a framework for building and solving battery models
Models
Lithium-ion models (full and reduced-order)
Lead-acid models
Fully coupled thermal models
Degradation mechanisms (SEI)
Library of Chemistries / Parameters
LCO, LiNiCo02, NCA, NMC
Graphite
LiPF6 ​
Easy to add your own parameter sets
Functionality
Range of numerical methods for solving models
Choice of cell geometries: 1D, 2+1D single layer pouch cells
Interface with external software
Experimental suite
Any voltage, current or power control, for example:
  GITT, PITT, CCCV, drive cycle
Easy interface to define custom protocols

## Slide 11: Flexible Submodel Structure
r
x
r
x
PyBaMM includes popular battery model such as the Doyle-Fuller-Newman model (P2D) and the Single Particle Model
Stefan
Maxwell
Fickian Diffusion
Lumped Thermal
Custom Model
Users can build custom models from submodels
Battery models are constructed from submodels
Use or adapt pre-built models
Create custom models

## Slide 12: Flexible Submodel Structure
Structure allows for
“plug and play” physics
New physics can be quickly implemented in an independent fashion
Different physical mechanisms are readily included in both full and reduced-order models
Using PyBaMM it is easy to compare how different physics affects the model solution. Here we investigate the influence of different models for the particles (Fickian diffusion, and three reduced-order polynomial approximations [Subramanian et al., 2005]).

## Slide 13: PyBaMM Pipeline
Choice of spatial discretisation
  Finite Volume Method
  Spectral Volume Method
  Finite Element Method
Multiple ODE and DAE solvers (e.g. scipy, sundials CVODE and IDA)
Obtain Jacobians via automatic differentiation
[Work in progress] Sensitivity analysis via automatic differentiation
By employing a pipeline process PyBaMM separates the statement of model equations from the inputted parameters, choice of spatial discretization and choice of time stepping algorithm.
Martin Robinson, Oxford RSE

## Slide 14: Simple Interface: CC Discharge
Easy interface for running simulations
Both model and simulation can be customised

## Slide 15: Simple Interface: Change parameters
Easy to change parameters and model options

## Slide 16: Parameter Library
Library of parameter values including popular chemistries such as LiNiCo02, NMC, Graphite, LiPF6
Choose by component (anode, cathode, etc.) or pick a complete parametrization from ​a given reference
Easy to “tweak” existing parameter sets or add your own from scratch
Development of Experimental Techniques for Parameterization of Multiscale Lithium-ion Battery Models, Chang-Hui Chen, Ferran Brosa Planella, Kieran O’Regan, Dominika Gastol, W. Dhammika Widanage and Emma Kendrick, Journal of The Electrochemical Society, 2020
Parameterization of a physico-chemical model of a lithium-ion battery II. Model validation, Madeleine Ecker, et al, Journal of The Electrochemical Society, 2015

## Slide 17: Simple Interface: Experimental protocol
PyBaMM allows users to specify experimental protocols using keyword strings
Can easily define custom protocols
Specify current, power or voltage

## Slide 18: Simple Interface: Experimental protocols & drive cycles

## Slide 19: Fast Solve Times
A comparison of typical solve times for different models and disrectisations for a 1C constant current discharge.
An asymptotic derivation of a single particle model with electrolyte, S.G. Marquis, V.Sulzer, R. Timms, C.P. Please and S.J. Chapman, Journal of The Electrochemical Society 2019
Grid points per domain | Single Particle Model |  | Doyle-Fuller-Newman Model | 
 | States | Time (milliseconds) | States | Time (milliseconds)
10 | 21 | 3 | 281 | 72
20 | 41 | 3 | 961 | 149
40 | 81 | 4 | 3251 | 384
80 | 161 | 5 | 13441 | 1293
160 | 321 | 9 | 52481 | 7689
All simulation performed on a laptop computer (i5, 2.1 GHz, 16 Gb of RAM) using the CasADi solver with both absolute and relative tolerances of 10-6 . The parameters are from the reference:

## Slide 20: Fast Solve Times
A comparison of typical solve times for different models and disrectisations for the US06 drive cycle
Grid points per domain | Single Particle Model |  | Doyle-Fuller-Newman Model | 
 | States | Time (seconds) | States | Time (seconds)
10 | 21 | 0.03 | 281 | 4.01
20 | 41 | 0.03 | 961 | 7.53
40 | 81 | 0.04 | 3251 | 20.30
80 | 161 | 0.07 | 13441 | 66.19
160 | 321 | 0.10 | 52481 | 247.15
All simulation performed on a laptop computer (i5, 2.1 GHz, 16 Gb of RAM) using the CasADi solver with both absolute and relative tolerances of 10-6 . The parameters are from the reference:
An asymptotic derivation of a single particle model with electrolyte, S.G. Marquis, V.Sulzer, R. Timms, C.P. Please and S.J. Chapman, Journal of The Electrochemical Society 2019

## Slide 21: CASE STUDIES

## Slide 22: Case Study: Single Particle Model with electrolyte (SPMe)
Systematic derivation of SPMe using asymptotic methods
Outperforms other (ad hoc) models in literature of similar complexity
Achieves order of magnitude reduction in computation cost at small loss of accuracy
Extends the validity of SPM to higher C-rates.
Electrolyte diffusion time << discharge time
Large electrode and electrolyte conductivity
An asymptotic derivation of a single particle model with electrolyte, S.G. Marquis, V.Sulzer, R. Timms, C.P. Please and S.J. Chapman, Journal of The Electrochemical Society 2019

## Slide 23: Case Study: Reduced order pouch cell modelling
Larger batteries exhibit non-uniform behaviour which may adversely affect battery performance and lifetime
Exploit the geometry to systematically derive 2+1D model
Combine with other limits to derive a hierarchy of reduced-order models
Influence of cell geometry can be investigated efficiently
Numerical validation against “full” model in COMSOL
Asymptotic Reduction of a Lithium-ion Pouch Cell Model, R. Timms, S.G. Marquis, V.Sulzer, C.P. Please and S.J. Chapman, Submitted to SIAM Journal on Applied Mathematics
A Suite of Reduced-Order Models of a Single-Layer Lithium-ion Pouch Cell, S.G. Marquis, R. Timms, V.Sulzer, C.P. Please and
S.J. Chapman, Submitted to Journal of the Electrochemical Society

## Slide 24: Case Study: Reduced order pouch cell modelling
Asymptotic Reduction of a Lithium-ion Pouch Cell Model, R. Timms, S.G. Marquis, V.Sulzer, C.P. Please and S.J. Chapman, Submitted to SIAM Journal on Applied Mathematics
A Suite of Reduced-Order Models of a Single-Layer Lithium-ion Pouch Cell, S.G. Marquis, R. Timms, V.Sulzer, C.P. Please and
S.J. Chapman, Submitted to Journal of the Electrochemical Society
Example result: 10x10 grid of Single Particle Models with fully coupled thermal effects. Approximate solve time: 9s

## Slide 25: Case Study: A coupled multiscale model of electrochemistry and thermal transport for Li-ion cells
Internal temperature differences lead to non-uniformities in current flow, state of charge, particle stress and levels of degradation
Li-ion battery heat generation and transport problem coupling:
  particle scale electrochemical modelling (PyBaMM)
  cell level electrical and thermal modelling (OpenPNM)
Example: a 2D heat-transfer problem for spirally rolled cylindrical batteries using tomography data
Probing heterogeneity in Li-ion batteries with coupled multiscale models of electrochemistry and thermal transport using tomographic domains, T.G. Tranter, R. Timms, T.M.M. Heenan, S.G. Marquis, V. Sulzer, A. Jnawali, M.D.R. Kok, C.P. Please, S.J. Chapman, P.R. Shearing, D.J. L. Brett, Journal of The Electrochemical Society, 2020

## Slide 26: Case Study: A coupled multiscale model of electrochemistry and thermal transport for Li-ion cells
Probing heterogeneity in Li-ion batteries with coupled multiscale models of electrochemistry and thermal transport using tomographic domains, T.G. Tranter, R. Timms, T.M.M. Heenan, S.G. Marquis, V. Sulzer, A. Jnawali, M.D.R. Kok, C.P. Please, S.J. Chapman, P.R. Shearing, D.J. L. Brett, Journal of The Electrochemical Society, 2020
HTC = 5 [W.m-2]
σ = 3e7 [S.m-1]
#tabs = 5
Current = 5 [A]

## Slide 27: Case Study: SEI models
SEI models for:
constant SEI thickness
reaction limited
solvent-diffusion limited
electron-migration limited
interstitial-diffusion limited
EC-reaction limited
Example: loss of lithium to negative electrode SEI using the interstitial-diffusion limited model with different initial SOCs

## Slide 28: Case Study: Thermal runaway under external short-circuit
Simulate external short-circuit by imposing resistance
Add decomposition of SEI, anode, and cathode to SPM
Lumped thermal model
Good agreement with experiments
Model provides additional physical insight
External short circuit performance of Graphite-LiNi1/3Co1/3Mn1/3O2 and Graphite-LiNi0. 8Co0. 15Al0. 05O2 cells at different external resistances, A. Kriston et al, Journal of Power Sources, 2017
For more information, contact Vivian Tran, Department of Mechanical Engineering, University of Michigan
Experiment (Kriston et al)
Simulation
Experiment (Kriston et al)
Simulation

## Slide 29: Case Study: Thermal runaway under external short-circuit
For more information, contact Vivian Tran, Department of Mechanical Engineering, University of Michigan

## Slide 30: Case Study: Understanding LFP degradation
Work led by Daniel Albamonte, University of Michigan. For more information contact Dr V Sulzer, Department of Mechanical Engineering, University of Michigan
﻿Data-driven prediction of battery cycle life before capacity degradation, K.A. Severson et al., Nature Energy, 2019
Recent work by Severson et al. shows that features from discharge voltage curves can be used to predict cycle life
Use PyBaMM to fit DFN model to battery data, giving excellent agreement
Changing the anode diffusion coefficient produces features as seen in the data

## Slide 31: Case Study: Variational Bayes
For more information contact Antti Aitio, Battery Intelligence Lab, University of Oxford
Wrapping pymc3, a Bayesian library, around PyBaMM’s SPMe
Generate synthetic data with noise
Use Variational Bayes to recover probability distributions for electrolyte conductivity and transference number

## Slide 32: Highlighted upcoming feature: pack modelling using PyBaMM and Simulink
Black box PyBaMM model put in Matlab system
Linked in circuit with busbar and connection resistances
Pack level electrical and thermal problem solved in Simulink
Casadi solver used to efficiently call battery functions
Input currents and temperatures
Output heat and voltage sources and internal resistance calculated with physics based models
For more information contact Dr T Tranter, UCL Electrochemical Innovation Lab

## Slide 33: Highlighted upcoming feature: Integration with Julia
For more information contact Dr V Sulzer, Department of Mechanical Engineering, University of Michigan
Create symbolic model
PyBaMM
Create symbolic model (ModelingToolkit.jl)
Discretize (DiffEqOperators.jl)
Solve ODEs/DAEs
(DifferentialEquations.jl)
Julia (SciML)
Solve Physics-Informed Neural Network
(NeuralPDE.jl)

## Slide 34: Upcoming features
Work commenced
Planned work
Future work
Sensitivity analysis & parameter estimation
Simulink interface
Particle size distribution
Other chemistries (LiS)
Different particle shapes
Lithium plating
Fuel cells
Mechanics coupled to temperature and lithiation
Solid-state battery models
Improvements to framework
Other geometries (jelly rolls, multiple layer cells, etc.)
Integration with open battery database, parameter database
… your ideas?

## Slide 35: Further information – pybamm.org

## Slide 36: Contributors

## Slide 37: USING PYBAMM

## Slide 38: How to use PyBaMM? Ways to engage
Try online
Use PyBaMM in your browser without any installation.
Develop
Clone git repository to
contribute code.
Install locally
Install PyBaMM on your computer.

## Slide 39: How to use PyBaMM? Training resources
Lots of new resources online at
pybamm.org/getting-started
Training delivered via Faraday masterclass and tech series training
  Recordings and resources available online
  Over 50 attendees
Getting Started notebooks
  Run in your browser via Google Colab -- no need to install PyBaMM!

## Slide 40: Google Colab
Online tutorials run interactively in your browser using Google Colab, removing the need to install PyBaMM locally

## Slide 41: Contributing
Create an issue where new proposals can be discussed before any coding is done
Create a branch of PyBaMM on your own fork where all changes will be made
Implement your work
Add relevant references to CITATIONS.txt
Register these in the parts of the code that use your paper
Test your code!
Create a pull request to merge into the main code when you are ready for your code to be publicly available
If you would like to work on something in private please get in touch!

## Slide 42: How to ensure your contribution is credited
Example: Ferran Brosa Planella, WMG
Added LGM50 parameter set on his own fork
Added reference to relevant paper
Merged into main code
When the parameters set “Chen2020” is used, PyBaMM returns the citation
PyBaMM generates BibTeX entries for the papers cited in the script